## Slide 1
MS-PhD Program of Mechanical Engineering
Seoul National University, South Korea
Jiwon Kang
PINN Papers Summary

## Slide 2
2. GOALS
2. TOuNN
1. TO+GAN

## Slide 3
    Main Idea
2. TOuNN
1. TO+GAN
Drawbacks in conventional Generative Design (TO)
- Do not use AI
- Unable to create aesthetic designs but only focus on engineering performance
- Low diversity
Drawbacks of the Generative models (VAE, GAN, Auto-Encoder)
- Difficult to access industrial training data
- Cannot guarantee feasible engineering
- Model collapse (training instability)
Topology optimization
Generative Models

## Slide 4
    Methodology
2. TOuNN
1. TO+GAN
Stage1: collect previous designs in the market/industry as reference designs

## Slide 5
    Methodology
2. TOuNN
1. TO+GAN
Stage2: obtain new designs with TO
2. SIMP (solid isotropic material with penalization) -> well used TO method
1. objective of TO
compliance minimization (engineering performance)
pixel wise L1 distance minimization (aesthetic performance, diversity)
calculate material density with minimum compliance related to the stiffness

## Slide 6
    Methodology
2. TOuNN
1. TO+GAN
Stage3, 6: filter out by the similarity criterion (using L1 distance) → reduce computation
Stage4: if the ratio (# of new designs / # of total designs) smaller than threshold → exit the iterative design exploration → to stage8
Stage5: create new designs by generative models → also reference designs for TO in stage 2
Use BEGAN (boundary equilibrium GAN)

## Slide 7
    Methodology
2. TOuNN
1. TO+GAN
Results from BEGAN

## Slide 8
    Methodology
2. TOuNN
1. TO+GAN
Stage7: train auto-encoder with data from stage1 → auto-encoder learn the features of the reference data
→ designs similar to the reference show good reconstruction, dissimilar ones don’t → evaluate design novelty
Few FP, FN
Shows the robustness of the auto-encoder
→ Novelty of our design can be well defined

## Slide 9
    Result
2. TOuNN
1. TO+GAN
Stage8: Evaluate 3 design attributes (novelty, cost, compliance)
3D models from 2D design

## Slide 10
    Result
2. TOuNN
1. TO+GAN
TO without the reference designs from stage 1
TO without BEGAN (reference only from stage 1)
cannot yield aesthetical diversity
Poor Results from other generative models

## Slide 11
    Pros and Cons
2. TOuNN
1. TO+GAN
- Considers engineering performance and also aesthetics (novelty)
- Large number of designs starting from a small number of designs
- Diversity of designs
- Data generated from BEGAN passes TO → instability of generative models are solved
→ robustness of the quality can be guaranteed
Pros
Cons
- Gray area (density not 1 or 0) still exists
- Disconnections still exist

## Slide 12
2. GOALS
2. TOuNN
1. TO+GAN

## Slide 13
    Main Idea
2. TOuNN
1. TO+GAN
Drawbacks in previous DL applied Generative Design (TO)
- Use NNs only to accelerate topology optimization
-> This work directly execute TO using NNs

## Slide 14
    Methodology
2. TOuNN
1. TO+GAN
Neural Network
- output of NN: density value at a point
- softmax at the end to ensure the density to lie between 0 and 1
- Glorot normal initialization for weight/bias
FEA (Finite element analysis)
- regular 4 node quad element
- fast Cholesky factorization based on the CVXOPT library
- compute the stiffness matrix for each element based on the density at the center of the element
→ assemble global stiffness matrix → compute displacement vector u, compliance of each element
→ compute total compliance
3. Loss function
alpha: penalty parameter, J0: initial compliance
alpha → start from a small positive value → increase iteratively

## Slide 15
    Methodology
2. TOuNN
1. TO+GAN
Algorithm
- initialize the penalty parameter alpha, SIMP parameter p
- compute element densities with NN
- FE solve to calculate compliances
- compute the loss function and the gradients
- update weight/bias and the parameters
- repeat until termination → when the percentage of gray elements is less than a threshold

## Slide 16
    Experiments
2. TOuNN
1. TO+GAN
Effect of mesh size
Expandability to higher resolution

## Slide 17
    Experiments
2. TOuNN
1. TO+GAN
Extensions to 3D
Ease of additional design/manufacturing constraints
Symmetry
Non-design region
Extrusion

## Slide 18
    Pros and Cons
2. TOuNN
1. TO+GAN
- Ease application to higher resolution
- Extensions to 3D
- Ease of additional constraints
Pros
Cons
- Fail to converge for distributed load problem
- Twice computational cost compared to SIMP
- Lack of detailed features